SDP Platform Guide

Arduino
OS/Environment:- ArduinoIDE – Installed on DiCE -command line:- arduino
Programming:- Arduino C++
Communication:- RF Module built in and supplied RFstick for PC (see associated RF guide for settings)
Pros:- Best for IO devices, widest range of sensors available.
Cons:- Limited processing speed, memory and communication options

EV3
OS/Environment:- EV3DEV
Programming:- Python
Communication:- Wireless (with provided WiFi USB stick – using SDPRobots network). Bluetooth (Built in)
Pros:- Best option for driving motors and ease of use for standard Lego sensors
Cons:- Slower and less memory than the RPI, limited range of sensors available

Raspberry Pi
OS/Environment:- Raspian
Programming:- Python. Sandbox environment – pre-installed – see associated programming guide
Communication:- Wireless & Bluetooth (Built in)
Pros:- Best option for using cameras with the fastest processing and largest memory available.
Cons:- GPIO can be fragile – No direct analogue input

Case Examples

Hospital Based Secure Delivery Robot :-
A robot could use all 3 platforms interlinked via their USB cables.
The EV3 using a colour sensor for line detection and driving the motors.
The Raspberry PI doing image processing from the camera as well
as the main onboard processing, communication with both the other platforms and the APP and DiCE computer.
The Arduino ran the Infrared distance sensors, the bump switches, controlled the electromagnetic lockbox.

Robotic School Road Crossing Guard:-
The robot used an EV3 for its drive motors and colour sensor to see the road markings.
The Raspberry Pi handled the processing, the communication and the crossing message display module.
The arduino was used as part of the environment, receiving input signals from the force sensors which were detecting the traffic and output control signals to the traffic and crossing lights.